## Slide 1
Training module 1
The CESBA MED Generic Framework concept and the multicriteria
assessment methodology

## Slide 2: Why we talk about sustainability?
Europe, cities:
- 70% of energy consumptions
- 60-70% of total CO2 emissions
- the highest number of population
CO2 concentration
Temperature
Sea level
Resources
Fuels
Energy
IMPACTS ON POPULATION AND CITIES

## Slide 3: Why we talk about sustainability?
Buildings use and construction
(EC COMM 445)
40% CO2 Emissions
50% Energy Consumptions
50% Extracted Materials
30% Water Consumptions
30% Waste Production
What can we do to reduce the impacts?
INCREASE SUSTAINABILITY of buildings and urban areas
Improving the existing built
Adressing the new projects

## Slide 4: Sustainable Development
UNITED NATIONS
AGENDA 2030 FOR SUSTAINABLE DEVELOPMENT
17 Macro Targets of sustainable development
169 Specific Targets
UN General Assembly
25 September 2015

## Slide 5: Sustainable Development

## Slide 6: Sustainability of urban areas
ENHANCING SUSTAINABILITY IS A CHALLENGE THAT REQUIRES SYNERGIC ACTIONS, STRATEGIES, PROJECTS AND POLICIES.
Three big themes with a long-term perspective:
Urban system
Environment
Society and Economy
Many options on which to operate:
Quality and accessibility
Techologies and performances
Materials
Processes
Land and resources
Impacts and ecology
Social and economic

## Slide 7: Who are interested in urban areas sustainability?
.
Public Istitutions
Investors
Companies
Owners
Research Istitutions
Designers
Users
Public
Administration
Market
Industry
Research and
Academy

## Slide 8: Urban vs building scale
Energy efficient measures and their implementation at district level allow to reach significant and cost-effective improvements compared to a building scale approach.
Urban scale approach is frequently the most efficient one:
synergies among buildings
wasted energy exploitation
efficient use of renewable energy sources
cogeneration systems
economy scale factor.
Thinking building by building is not efficient !

## Slide 9: Decision making at urban scale
Main features:
High complexity
Large number of stakeholders involved
Complex value chain
Many variables to take in account

## Slide 10: The CESBA MED – Sustainable cities project
Development and testing a transnational system to assess urban sustainability
Transfering the assessment system through a training system
Capitalizing the assessment system promoting the adoption by public administrations

## Slide 11: The CESBA MED – Sustainable cities project
Main Objectives
Harmonize assessment systems in Europe
Foster the adoption of the assessment tools by public administrations
Enhance the sustainability of built environment

## Slide 12: The CESBA MED principles
The Generic Framework is perfectly in line with 9 CESBA principles:
Users
Sustainability
Contextualization
Comparibility
Mass approach
Ease of use
Open source
Collaboration
Trasparency

## Slide 13: The CESBA MED Generic Framework
Transnational generic multicriteria assessment tool :
to rate the level of sustainability of buildings and urban areas
to create urban and buildings assessment tools
Generic: in order to be used, the system must be contextualised
Tools, deriving from the same source, are harmonized and they produce comparable results

## Slide 14: Performance Assessment
Performance analysis with regards to a group of criteria and indicators
Rating of a urban area on the base of its performance
Procedure
Score and rating
Results
Objective

## Slide 15: The CESBA MED – Assessment tool
Assessment tool for urban areas
Applicable to existing and new areas
Including all the stages of the life cycle
Support the planning activities from definition of targets to check of results
PHASES
Block
SCALE
Neighborhood
District
Existing
Project
Monitoring

## Slide 16: What is innovative in CESBA MED?
Rating/Assessment tools at urban scale for existing neighbourhoods
Rating/Assessment tools fully contextualized
Integration of the building scale and urban scale assessments in a unique decision making process
Possibility to consider the building in the context of its surrounding area
Assessment systems designed to fit public administrations’ needs. Not for market purposes
Comparibility, mass approach, ease of use, transparency and collaboration

## Slide 17: Why assessment tools?
Provision of objective and reliable information to support decision making processes.
Possibility to set reliable, measurable and verifiable performance targets for urban areas and buildings, based on quantitative indicators.
Provision of a reference common framework for the stakeholders
Easy comparison among urban areas and countries
Easy communication among stakeholders
Development of a common vocabulary for environmental assessment

## Slide 18
1 TRANSNATIONAL GENERIC FRAMEWORK
8 CONTEXTUALIZED LOCAL TOOLS

## Slide 19
Assessment tools to:
FIX TARGETS
OBJECTIVE
CREDIBLE
MEASURABLE
VERIFIABLE
TO ADRESS THE ACTIONS

## Slide 20
Assessment tools for:
POLICIES
REGULATIONS
INCENTIVES
GREEN PUBLIC PROCUREMENT
URBAN PLANS
ACTION PLANS

## Slide 21: Based on existing knowledge
NO NEW INDICATORS!
TEST OF EXISTING SETS OF INDICATORS FROM:
EU PROJECTS
URBAN SCALE ASSESSMENT TOOLS
EU FRAMEWORK OF COMMON INDICATORS

## Slide 22: 12 Partners – 7 Countries
Città di Torino - Italy
iiSBE Italia R&D - Italy
Città di Udine – Italy
EnvirobatBDM - France
AURA EE - France
Metropolitan City of Marseille – France
Government of Catalonia - Spain
Municipality of Sant Cugat del Vallés – Spain
University of Malta – Malta
National Observatory of Athens – Greece
Energy Institute Hrvoje Požar – Croatia
CESBA – Austria
Start: November 2016
End: October 2019
Project value: 3.190.375 euros

## Slide 23: 7 EU Projects - Building scale
ENERBUILD
CABEE
CEC5
OPENHOUSE
SUPERBUILDINGS
EPISCOPE
IRH MED

## Slide 24: Assessment tools – Building scale

## Slide 25: EU COMMON FRAMEWORK
EC COMM 445 (2014): Resource Efficiency Opportunities in the Building Sector
WG to study to identify an EU common framework of indicators to assess the environmental performance of buildings
iiSBE, RAEE, EnvirobatBDM members of the WG

## Slide 26: 4 EU Projects – Urban scale
FASUDIR
NewTREND
CLUE
CAT-MED

## Slide 27: 2 Assessment tools – Urban scale
PROTOCOLLO ITACA
QUARTIERS DURABLES MEDITERRANEENS

## Slide 28
Reference scales: neighborhood
Traditional scale, culturally recognized (often not defined officially)
  City inhabitants recognize its defining traits (social, cultural, architectural)
Reference size values:
  Square with a 200-400 m size
  Area that can be crossed in 10-15 min walk
  200-1500 inhabitants
Appropriate scale for:
  Smaller scale networks (walking, cycling)
  Impact of buildings’ morphology on surroundings
  Local microclimate
  Daily services, social mix, segregation, equity, wellbeing, culture

## Slide 29
Reference scales: block
Easy to identify: defined by street intersections
  Oldest urban scale, also called cluster
  Can coincide with building scale, especially in recent developments
  Traditional composition: few buildings (adjacent or separated), internal courtyard
  5-15 buildings
Appropriate scale for:
  Detailed analysis of morphology
    Density, volume distribution, compactness…
  Energy characterization
  Precise microclimate studies
  In homogenous neighborhoods, representative blocks as benchmarks (for quick prototyping & simulation)

## Slide 30: The CESBA MED Generic Framework: SBEMethod
The assessment method adopted in CESBA MED Generic Framework multicriteria system is the SBEMethod (Sustainable Built Environment Method).
A generic multi-criteria analysis methodology for assessing sustainability of the built environment.
The method is organized in issues, categories and criteria
The sustainability score of assessment is computed through a mathematical procedure which is articulated in three steps:
Characterization
Normalization
Aggregation

## Slide 31: Assessment method
The performance score is computed through an assessment procedure articulated in 3 main steps:
Characterization
Normalization
Aggregation

## Slide 32: Characterization step
INDICATORS
NUMERICAL VALUE, REFERENCE SCENARIO
NUMERICAL VALUES (THE INDICATORS VALUES)
representing the urban area performances
Such values are determined starting from calculations, experimental measures, and through comparison with reference scenarios (in the case of qualitative criteria).
i.e. x Tons CO2/Km2 inhabitant, KWh/Km2 inhabitant, etc..

## Slide 33: Normalization step
DIFFERENT TYPOLOGY OF CRITERIA  DIFFERENT UNITS OF MEASURE
ADIMENSIONALIZATION AND RESCALING
NORMALIZED SCORES
values are included between -1 and +5
The methodology uses a linear normalization function for quantitative criteria.

## Slide 34: Normalization step
It’s possible to have three kinds of criteria:
HIB - Higher is better
The higher the indicator value, the better the performance level
LIB – Lower is better
The lower the indicator value, the better the performance level
Qualitative
Only discrete values, each of them is equivalent of a reference scenario defined by corresponding indicator

## Slide 35: Aggregation step
NORMALIZED SCORES associated with each criterion
WEIGHTED SUM
FINAL PERFORMANCE SCORE
Aggregation through criteria: all normalized scores of criteria in the same category are aggregated
Aggregation through categories: all normalized scores of categories in the same issue are aggregate
Aggregation through issue: all normalized scores of issues are aggregated

## Slide 36: Structure of the framework
The Generic Framework is organized in:
Issue = macro-theme chosen and recognised as relevant for assessing the sustainability of a building or urban area (i.e. Built Urban System)
Category = a particular aspect pertaining to a specific issue (i.e. Urban Structure and Form)
Criterion = specific aspect of relative category. They represent the basic assessment entries used to characterize each building or urban area since the very beginning of the assessment process. (i.e. Concentration of land parcels)
Each criterion is associated to an indicator.
Indicator = methodology which allows to characterize the building performance.

## Slide 37
Hierarchical structure of the framework

## Slide 38
The Generic framework – URBAN SCALE
7 ISSUE
23 CATEGORIES
178 CRITERIA AND INDICATORS

## Slide 39
Issues
A – Built Urban System
B – Economy
C – Energy
D – Atmosperic Emissions
E – Non-Renewable Resources
F – Environment
F – Social Aspects

## Slide 40
Issues and Categories
A – Built Urban System
A1 – Urban Structure and Form
A2 – Transportation Infrastructure
B - Economy
B1 – Economic Structure and Value
B2 – Economic Activity
B3 – Cost and Investment

## Slide 41
Issues and Categories
C - Energy
C1 – Non-Renewable Energy
C2 – Renewable and Decarbonised Energy
D – Atmosperic Emissions
D1 – Atmospheric Emissions
C3 – Energy Recycling and Storage

## Slide 42
Issues and Categories
E – Non-Renewable Resources
E1 – Potable Water, Stormwater and Greywater
E2 – Solid and Liquid Wastes
E3 – Resource Consumption, Retention and Maintenance
F - Environment
F1 – Environmental Impacts
F2 – Outdoor Environmental Quality
F3 – Ecosystems and Landscapes

## Slide 43
Issues and Categories
G – Social Aspects
G3 – Communication Services
G4 – Public and Private Facilities and Services
G5 – Local Food
G1 – Safety and Accessibility
G2 – Traffic and Mobility Services
G6 – Management and Community Involvement
G7 – Society, Culture and Heritage
G8 – Perceptual

## Slide 44
Issues, Categories and Criteria

## Slide 45: Definitions
Criterion: an assessment item which permits to analize a specific performance. All criteria are performances. In order to make a certain criterion operative, it is necessary to combine it with a physical quantity or scenario: the indicator.
Indicator: physical quantity or qualitative scenario that allows to quantify the performance with respect to an assessment criterion. Quantitative indicators have a unit of measure.

## Slide 46: Examples of criteria
Examples of criteria, indicators and relative units of misure
CRITERION | NAME | INDICATOR | UNIT OF MISURE
A2.6 | Connectivity of the street network | Number of intersections present in the analyzed area related to the overall surface area | n/km2
B2.3 | Employment rate | Percent of working age adults in the local area who are employed or actively looking for work. | %
C1.1 | Total final thermal energy consumption for building operations | Urban thermal energy consumption of all buildings | kWh/m2

## Slide 47: Criteria distribution
Chart: 
| A - Built Urban System | B - Economy | C - Energy | D - Atmospheric Emissions | E - Non-Renewable Resources | F - Environment | G - Social Aspects
Numero di criteri | 17 | 15 | 39 | 7 | 24 | 39 | 37

## Slide 48
AGENDA 2030
EU POLICIES AND TARGETS
REQUIREMENT TO COMPARE THE PERFORMANCES
AT TRASNATIONAL LEVEL
CESBA Sustainable Neighbourhoods Tool

## Slide 49
ASSESSMENT TOOLS MUST REFLECT
THE LOCAL PRIORITIES AND THE LOCAL CONTEXT
CESBA Sustainable Neighbourhoods Tool

## Slide 50
GENERIC FRAMEWORK (EU)
CONTEXTUALIZATION
ASSESSMENT TOOLS (FOR ANY CITIES)
Generated tools from Generic Framework are harmonized and comparable
CESBA Sustainable Neighbourhoods Tool

## Slide 51
CESBA Sustainable Neighbourhoods Tool
Transnational
Generic Framework
Tools
for the cities

## Slide 52: 9 Assessment Tool Test
9 assessment tools in test phase in:
Turin
Barcelona
Marseilles
Lyon
Athens
Zagreb
Sant Cugat del Vallés
Udine
Malta

## Slide 53: City morphology
CITY MORPHOLOGY
LEVEL 1:
People and activities
LEVEL 2:
Connections and street network
LEVEL 3:
Urban blocks
LEVEL 4:
Site topography
LEVEL 5:
Land use
LEVEL 6:
Weather conditions

## Slide 54
Regional tool creation
CESBA MED SN GENERIC FRAMEWORK
ASSESSMENT METHODOLOGY AND CRITERIA
1. CRITERIA SELECTION
2. PERFORMANCE SCALES DEFINITION
3. WEIGHTS ASSIGNMENT
LOCAL
CONTEXT
CITY OF TURIN TOOL

## Slide 55
To contextualize the generic framework and produce a SN local tool is necessary to follow 3 steps:
Select the active criteria
from the whole list of the CESBA GF. Only the KPIs are mandatory for all local SNTool. There isn’t a minimum number of criteria to be selected.
Define benchmark for criteria
consist in the definition of the scoring scale for each criterion selected (from -1 to +5)
Weight assignment to criteria
categories and issues (%). The final total score denotes the global performance of the urban area or the building.
Regional tool creation: contextualization

## Slide 56: Contextualization: 1- criteria selection
SELECTION OF ISSUES, CATEGORIES AND CRITERIA TO USE FROM GENERIC FRAMEWORK.
THE SYSTEM IS MODULAR.
THE AVERAGE NUMBER OF CRITERIA IS 40-50.

## Slide 57: Contextualization: 2- performance scale definition
Laws/regulations
Technical legislation
Literature
Statistics data
Simulations
ASSOCIATION OF A SCORE TO
THE INDICATOR VALUE
Performance | Score
NEGATIVE PERFORMANCE | -1
MINUMUM ACCEPTABLE PERFORMANCE | 0
Moderate improvement of the performance compared to the current practice | 1
Substantial improvement of the performance compared to the current practice | 2
BEST CURRENT PRACTICE | 3
Increase of best current practice | 4
EXCELLENCE | 5

## Slide 58: Contextualization: 2- performance scale score
0 = MINIMUM = 50
50
180
0
5
90
5 = EXCELLENT = 180
A2.6 Connectivity of the street network [intersections/km2]

## Slide 59: Contextualization: 3- weight assignment to criteria
A1.7
Conservation of land

## Slide 60: Contextualization: 3- weight assignment to criteria
CRITERIA
B1.1 | 25%
B1.2 | 75%
B3.1 | 33%
B3.2 | 67%
B3.1 | 26%
B3.2 | 11%
B3.3 | 6%
B3.4 | 11%
B3.5 | 26%
B3.6 | 11%
B3.7 | 9%
B6.2 | 50%
B6.3 | 50%
B1 - Energy | 35%
A - Environment | 21%
B - Resources | 21%
C - Services | 17%
D - Society | 8%
E - Economy | 25%
B2 - Water | 15%
B3 - Material | 15%
B5 - Land | 20%
B6 - Buildings | 15%
CATEGORIES
ISSUES

## Slide 61: Contextualization: 3- weight assignment to criteria
Issues scores
Final
score

## Slide 62: Contextualization: 3- weight assignment to criteria
CURRENT STATE
TARGETS

## Slide 63: Contextualization: CESBA MED Software
GENERIC FRAMEWORK
REGIONAL TOOL

## Slide 64: CESBA SN Tools
B - Economy
C - Energy
D – Atmospheric Emissions
A – Built Urban System
E – Non-Renewable Resources
F – Environment
G –Social Aspect
Optional criteria
KPI

## Slide 65: CESBA SN Tools – KPI
A – Built Urban System
B - Economy
C - Energy
D – Atmospheric Emissions
E – Non-Renewable Resources
F – Environment
G –Social Apsect
Optional criteria
KPI

## Slide 66: CESBA SN Tools – KPI
torino
TURIN
BARCELONA
MARSEILLES
ATHENS

## Slide 67: KPIs
COMMON COMPUTATION METHODOLOGIES = COMPARABLE RESULTS
KPIs
Soil
Water
Emissions
Waste
Energy
Pollution
Mobility
Services
Energy cost
Partecipation

## Slide 68: KPIs
A – Built Urban System
A 1.7 Conservation of land
B.3.3 Use stage energy cost for public buildings
B - Economy

## Slide 69: KPIs
C.1.1 Total final thermal energy consumption for building operations
C.1.4 Total final electric energy consumption for building operations
C.1.7 Total primary energy demand for building operations
C.2.1 Share of renewable energy on-site, on total final thermal energy consumptions for buildings operation
C.2.7 Share of renewable energy on-site, on final electric energy consumptions
C - Energia

## Slide 70: KPIs
D – Atmospheric Emissions
D.1.2 Total GHG Emissions from primary energy used in building operations
E.1.6 Consumption of water for residential population
E.1.7 Consumption of water for non-residential building systems
E – Non-Renewable Resources

## Slide 71: KPIs
F - Environment
G.2.1 Performance of the public transport
G.2.4 Quality of pedestrian and bicycle network
G – Social Aspects
F.1.3 Recharge of groundwater through permeable paving or landscaping
F.2.3 Ambient air quality with respect to particulates <10 mu (PM10) over a one-year period
G.4.2 Availability and proximity of key services
G.6.3 Community involvement in urban plannig activities

## Slide 72: KPIs
Chart: KPIs distributed in issues
| A - Built Urban System | B - Economy | C - Energy | D - Atmospheric Emissions | E - Non-Renewable Resources | F - Environment | G - Social Aspects
Colonna1 | 17 | 15 | 39 | 7 | 24 | 39 | 37
Serie 2 | 1 | 1 | 5 | 1 | 2 | 2 | 4

## Slide 73: CESBA MED Passport
A Passport for Buildings and Neighbourhoods to:
Transnationally compare the assessment results
Make easier sharing best practices
Measure the contribution to common objective
→ HARMONIZATION
COMMON METRICS FOR KEY ISSUES !
Generate harmonized assessment tools
A common indicators set to facilitate comparison

## Slide 74: CESBA MED Passport
TRANSNATIONAL
DOCUMENT
ASSOCIATED WITH LOCAL
TOOL ASSESSMENT
+
+
TORINO TOOL SCORE
BARCELONA TOOL SCORE
KPIs
KPIs

## Slide 75: CESBA MED Passport
BARCELONA TOOL SCORE
SAME COMPARABLE
MEANING
KPIs
TORINO TOOL SCORE

## Slide 76: CESBA MED Passport
W
THINK GLOBAL
KPIs
ASSESSMENT OF LOCAL POLICIES REFERS TO GLOBAL TARGETS
CONNECTION BETWEEN GLOBAL AND LOCAL LEVEL
@Andrea Moro
ACT
LOCAL

## Slide 77: DG Environment and CESBA MED
Testing new Level(s)
system on public buildings
Interview on YouTube - EU Environment

## Slide 78: WSBE Hong Kong 2017
Presentation of results at the WSBE 2017 World Conference in Hong Kong
Synergy with non-European iniziatives: URBENERE (South America), Districts 2030 (North America)

## Slide 79
Introduction of CESBA Passport to Unity “Cities” of UN Environment
Link to Passport SDGs
Meeting at UN Environment – Paris – January 2018

## Slide 80
THANKS !